## Slide 1
Observatory of Complex Systems
http://ocs.unipa.it
S. Miccichè
salvatore.micciche@unipa.it
A percolation approach for the detection of bottlenecks in air traffic networks
Università degli Studi di Palermo Dipartimento di Fisica e Chimica
Mathematical Models and Methods in Earth and Space Sciences
Tor Vergata, 21 March 2019

## Slide 2
work done in collaboration with:
Giuseppe Pappalardo and Rosario N. Mantegna
within the research project:
ADAPT - Advanced prediction models
for flexible trajectory-based operations
http://adapt-h2020.eu
PARTNERS:
SPONSORS:
Preface
Investigating a relevant socio-technical complex system with tools and methodologies of Statistical Physics, Network Science and Complex Systems.

## Slide 3
How the system works
STRATEGIC PHASE: planning of the trajectories
Accommodate as many as possible aircraft in a certain airspace, given the sectors capacity constraints
Origin O
Destination D
Sector 1
Sector 2
Sector 4
Sector 3
Sector 5
TACTICAL PHASE: managing the trajectories
Maintain the planned number of trajectories in each sector and avoid that they crash into each other;
Take into account congestions due to ground delays;
Take into account changes due to extreme weather events or STRIKES;
Take into account airspace closures due to existing military areas.

## Slide 4
The scientific question
MAIN OBJECTIVE 1: metrics for hotspots
We will help other WPs by providing metrics and methodologies for a statistically sound assessment of the bottlenecks/congestion present in the airspace.
Data will be fundamental.
Task 5.1.1:
Empirical investigation of aircraft trajectories

## Slide 5
Where data come from?
Data are provided by Eurocontrol that is the European agency that coordinates the activities of all European national agencies involved in the Air Traffic Management
EUROCONTROL is an intergovernmental organisation with 41 Member and 2 Comprehensive Agreement States. EUROCONTROL is committed to building, together with itspartners, a Single European Sky that will deliver the air traffic management (ATM) performance required for the twenty-first century and beyond.

## Slide 6
What data do we have?
M1 and M3 files: planned and actual trajectories data
M1
25 segments
M3
22 segments
01/06/2011 (unzipped)
Number of lines: 715753
M1 file
Size: 88M
Number of lines: 678006
M3 file
Size: 83M

## Slide 7
GSL files: sectors and airblocks
SPC files: collapsed sectors and sectors
GAR files: boundaries
What data do we have?
CFG files: configuration
COS files: opening scheme

## Slide 8
What data do we have?

## Slide 9
Aggregation
APAPT WP-5
Aggregate together all NVPs within a 5 km radius.
Exhaustive search – brute force
Computationally demanding
NVPs  agg-NVPs
1709898 210562
AIRAC 309 sett 2014

## Slide 10
APAPT WP-5
Aggregation
Agg-NVPs
NVPs

## Slide 11
Percolation
Percolation is the phenomenon by which a flow (of water) goes through a porous medium.
such fraction is called
order parameter
r=Vcavity/Vmedium
Formally: let us consider a rock which has many small cavities. Let us randomly place spherical cavities of radius r in a medium, allowing them to overlap. At what volume fraction of cavities is water able to travel arbitrarily long distances through the medium?

## Slide 12
Percolation
In our previous example we considered cavities distributed arbitrarily through space. It was an example of what is called continuum percolation.
Most of the percolation theory written down so far deals with percolation on lattices. For instance, consider a square grid. The chance that a given square is a “cavity” is a fixed probability, q.
The question is: what is the value of q such that one can go from one side of the lattice to another?
There is a general consensus that the percolation threshold on the square lattice is:
qc = 0.59274605

## Slide 13
Percolation
A student of mine: Physical Sciences Degree – Course on Informatics and Programming

## Slide 14
In general, percolation is a random process exhibiting a phase transition. In the simplest setting percolation is investigated in simple geometrical systems such as regular lattices covering a 2D surface.
One speaks about of node percolation the links of the lattice are always present between two occupied sites, but each site is occupied with probability q and empty with probability (1-q).
One speaks about bond percolation when a link between two neighboring sites is present with probability q and its absence is observed with probability (1-q). In this variant all sites are present in the system and links between any pair of them may or may not be present.
Percolation

## Slide 15
In our context, percolation refers to probabilistic, network-wide emergent behaviour, between sites.
Specifically, percolation refers to the phenomenon by which, according to the value of q, which play the role of an order parameter, the network shows a transition
from
a phase where all nodes are connected in a unique giant connected component
to
a phase where nodes belong to clusters of elements not connected between each others, i.e. the network gets fragmented.
Percolation

## Slide 16
APAPT WP-5
A Percolation approach in urban traffic
Network representation
of city roads
A very peculiar
network !!
NO

## Slide 17
APAPT WP-5
A Percolation approach in urban traffic

## Slide 18
APAPT WP-5
A Percolation approach in urban traffic

## Slide 19
APAPT WP-5
Network representation
of city roads
A much richer
network !!
What about our case?
For each ij pair:
Compute the inferred segment traffic load Qij(t) in a hourly
time window of a specific day
2) Compute the maximal segment traffic load Qmax(t) in a hourly
time window over an entire AIRAC cycle
3) Define rij=Qij(t)/Qmax(t)
4) Then make the thresholding
5) Then compute the size of the largest and second largest connected
component of the network
6) Then keep your fingers crossed !!!!
YES
A percolation approach in air traffic
Network representation
of NVP connections

## Slide 20
APAPT WP-5
A percolation approach in air traffic
It does not work !!!!

## Slide 21
A percolation approach in air traffic
12/09/2014 all 13:00 q=0.2
12/09/2014 all 13:00 q=0.5
12/09/2014 all 13:00 q=0.9
12/09/2014 all 13:00 q=0. (all links)

## Slide 22
APAPT WP-5
A percolation approach in air traffic
Why?
YES
NO
long-range links
short-range links
short-range links
Is it possible that long-range links keep the network connected even at large threshold values?

## Slide 23
A percolation approach in air traffic
Power-law with exponent close to 2
DECILES
MEDIAN
MEAN

## Slide 24
A percolation approach in air traffic
We are close, ….
Keep links with distance < 18.43 (1.38 minutes)

## Slide 25
A percolation approach in air traffic
We are close, ….
Keep links with distance < 23.29 (1.75 minutes)

## Slide 26
A percolation approach in air traffic
We are close, ….
Keep links with distance < 23.29

## Slide 27
5_th decile - 18.43
9_th decile - 82.50
8_th decile - 43.90
7_th decile - 30.63
6_th decile - 23.29
There is a dependence also from the
distance threshold
4_th decile - 14.77
A percolation approach in air traffic

## Slide 28
A percolation approach in air traffic
What is the interpretation of our results?
long-range links play a role: percolation seems to be a local effect !!
Percolation thresholds might be different in different time–intervals over a day
Also the distance threshold seems to be different in different time–intervals over a day
We are therefore able to detect links i j such that
IF the traffic load is at a certain percentage rij of their maximal traffic load Qij(t)
AND
IF such percentage is above a critical value qc
THEN the network may undergo the risk of getting fragmented into small disconnected parts.
The investigations we have so far performed, although preliminary, yet clearly shows that percolation occurs in the navigation balls network generated starting from the aircraft trajectories flying over the ECAC airspace in a certain day.
This approach is therefore able to detect links, characterized by certain q values, which carry a potential risk of disruption in the network.
Long-range links contribute to keep connected the air traffic network.

## Slide 29
A percolation approach in air traffic
12/09/2014 <23.29 km 13:00 q=0.2
12/09/2014 <23.29 km 13:00 q=0.5
12/09/2014 <23.29 km 13:00 q=0.9
12/09/2014 <23.29 km 13:00 q=0. (all links)

## Slide 30
A percolation approach in air traffic
12/09/2014 <30.63 km 13:00 q=0.2
12/09/2014 <30.63 km 13:00 q=0.5
12/09/2014 <30.63 km 13:00 q=0.9
12/09/2014 <30.63 km 13:00 q=0. (all links)

## Slide 31
A percolation approach in air traffic
12/09/2014 <30.63 km 13:00 q=0. (all links)
12/09/2014 <23.29 km 13:00 q=0. (all links)
Percolation
No Percolation
Size of network: 21159
Size of largest: 7354 (35%)
Size of second largest: 532 (2%)
Size of network: 22418
Size of largest: 12082 (54%)
Size of second largest: 1475 (7%)

## Slide 32
A percolation approach in air traffic
Where do we go from here 1 ?
Understand theoretically the role of long-range links and the interplay between long-range-ness and initial fragmentation.
Can we reproduce percolation & long-range links role at the level of:
  Erdos-Reny random networks?
  Preferential attachment networks?
  Core-periphery networks?
Can this help in understanding what is going on?
As a physicist I would be happy: lot of work for the months to come, … !!!!

## Slide 33
A percolation approach in air traffic
Where do we go from here 2 ?
We now have to think about the operational
consequencies of our results.
The most elementary operational units in ATM are Air traffic sectors
Air Traffic Sectors are characterized by Capacity
Sectors’ capacity is nowadays the most relevant issue when talking about the future of ATM.
Everybody is looking for a way to increase capacity, i.e a way to accomodate as many as possible aicraft in a certain airspace
Can we transpose percolation at the level of
AIR TRAFFIC SECTORS?

## Slide 34
A percolation approach in air traffic - sectors

## Slide 35
A percolation approach in air traffic - sectors
We need a resonable sectorization linked to the operational level
Node percolation?
Link percolation?
Work to be done

## Slide 36
Conclusions
Long-range links play an important role
percolation is a local effect
Interplay with initial fragmentation
understand why initial fragmntation does not necessarily imply percolation
We need to theoretically understand these issues
toy models with different network generating mechanisms
Percolation at the level of Air Traffic Sectors
node percolation vs link percolation - operational importance
A percolation approach in air traffic networks

## Slide 37
The End
salvatore.micciche@unipa.it

## Slide 38
Advertisement
We will have soon two open positions (expected in June 2019):
RTD-a FIS/07 – temporary lecturer
Complex Systems
Assegno di Ricerca – postdoc 18 months
funded by PRIN 2018
Stochastic forecasting in complex systems

## Slide 39
Advertisement
4.1 Econophysics
Why Physicists are interested in Financial Markets
Financial market can be considered as model complex systems
Many Agents/Factors
interactions are not always clear/known (NO equations, Hamiltonians, … )
G. Parisi cond-mat/0205297 Complex Systems: a Physicist's ViewPoint: “A system is complex if its behaviour crucially depends on the details of the system”
Econophysics is a “recently” established discipline whose main aim is that of modeling some of the stylized facts empirically observed in the study of financial markets.
We have a rich set of different databases.

## Slide 40
Methods of Statistical Physics and Network Theory can be applied :
Stochastic Processes (Brownian motion, superdiffusivity, power-law tails, long-range correlation,...)
scaling
Network theory, clustering techniques, random matrix, ...
Agent-based models, ...
...
Last but not least: There is a huge amount of data!
Advertisement

## Slide 41
Advertisement
4.2 BioStatistics
4.5 Methods
Stochastic Processes in Classical and Quantum Systems
Correlation-based Networks (MST, PMFG, ….)
Statistically Validated Networks
Community (Cluster) Detection and Characterization
Agent-based Models
4.4 Social Systems
Aged people in Europe
Criminal/Suspects in Sweden
Finnish Elections
News
Mobile phone communications
Gene Ontology
Inverted Repeats
MicroRNA
Complex Diseases
Personality traits of alexythimic patients
Characterization of Mafia communities
4.3 Socio-Technical Systems
Air Traffic Management
today’s talk