## Slide 1: Early Research Presentation
Optimal and Feasible Attitude Motions for Microspacecraft
Astronet School – Rome

## Slide 2: Background
Universitat Politecnica de Catalunya (UPC) – Aeronautical Engineering (specialization space vehicles)
CNES (2011-2012)
  Mission Rosetta: Lander’s descent trajectory optimization
  Long-term orbit propagator for space debris treatment (French Space Act). Resonances due to tesseral terms; modelling
  University of Strathclyde [Glasgow] – Marie‐Curie Early Stage Researcher within the AstroNet‐II Training Network – PhD (Oct 2012-2015)

## Slide 3: Overview
  Aim:
    Explore new ways of autonomous repointing (on-board planner) for micro- and nano- spacecraft
  Challenges:
    Limited torque, RW quick saturation  Optimal motions
    Low computational power available  Light algorithms
  Area: Motion Planning Attitude Control
Notes: Most of it has already been explained by Dr Biggs… so briefly:

## Slide 4: Outline of the work so far
  Attitude system: Reaction Wheels in the 3 orthogonal axis
  Current plan: 1) obtain an optimal trajectory, and 2) track it with a simple controller
  Main idea: To use close-to-optimal analytical motions as a good initial guess for numerical optimizers – path planning algorithms
  Analytical approaches:
    Spin-stabilized S/C: derivation of a parametric reference motion using geometric control theory – unconstrained parameter optimization (Dr. Biggs)
    Free motions of axisymmetric and asymmetric spacecraft (Pagnozzi & Maclean)
  Planner approach: To obtain feasible and optimal trajectories, optimal control problem solved using pseudospectral methods

## Slide 5: Analytical motions
  Biggs, J. D.: Optimal geometric motion planning for spin-stabilized spacecraft
    Functional optimization problem with quadratic cost function  Application of Pontryagin’s Minimum Principle  Integrable Hamiltonian system
    Angular velocities are trigonometric functions with 3 parameters (plus manoeuver time and/or spin speed)
  Pagnozzi & Maclean: Analytical solutions for free motion in quaternion form
    Solutions for the axisymmetric and asymmetric case (requires evaluation of Jacobi elliptic functions)
    Optimization parameters: initial angular velocities
  Fast parametric optimization to meet final position
  Analytical solutions usually do not meet real trajectory requirements, e.g. rest-to-rest, pointing constraints, etc
Notes: Biggs: as he said, solved a spinning satellite problem using the hamiltonian formulation on Lie groups. In the solution the angular velocities are trigonometric functions. You deal with 3 parameters and, if you want, you can add time and spin.
Daniele Pagnozzi and Craig Maclean, also strathclyde phd students, have done good work on free motions.

## Slide 6: Pseudospectral methods for O.C.
Optimal Control problem:
  Determine u(t), x(t) for a (constrained) dynamic system in order to minimise a performance index
PS methods for OC:
  Discretize an optimal control problem to formulate a NLP problem:
    Functions approximated using specific collocation points (roots of the time derivative of Legendre poly.)
    Differential equations approximated by system of algebraic equations
    Cost functional approximated by Gaussian quadrature
  Solved numerically to find local optimal solutions
  Software used: PSOPT (NLP solver: IPOPT, quasi-newton method)
Characteristics:
  Exponential (spectral) rate of convergence
  Accurate results with few nodes
  Importance of a good initial guess
  State of the art: being embedded in UAV for real-time planning
Notes: Analytial solutions are used as a good initial guess for a numerical optimizer.
My approach so far has been the use of pseudospectral methods for solving the optimal control problem.
Very basically, in the pseudospectral method we discretize the problem with carefully chosen nodes, to formulate a Nonlinear Programming problem.
Then, we solve it using a common numerical solver. So far I have been using a free software called PSOPT.
Pseudospectral methods are interesting to us because problem converges using few nodes or few iterations. So computationally speaking it’s appealing.
By the way, several studies show that a good initial guess is important for convergence, so this is an important part to work on.

## Slide 7: Some conclusions…
Analytically derived trajectories are (must be) quickly computed
Previous analytically derived trajectories are an initial guess for PSOPT  either the computation time or final optimization cost are improved
Promising approach – effort required to improve the quality of the initial guess, to be closer-to-optimal

## Slide 8: Future work
Short term:
  Explore other analytical initial guesses for PS methods – shape-based methods
  Try different planning algorithms – RRT*, MPC, only analytical…
  Combine actuators: RW + magnetorquers
Mid term
  Select and design a suitable planner algorithm
  Test robustness with accurate sensors, actuators, disturbances model
  Add DOF for translation motions: satellite inspection applications
Long term
  Implement and test
  Collaboration with Clyde Space
  Extrapolation to UAV systems

## Slide 9
Thanks for your attention
albert.caubet@strath.ac.uk